## Slide 1: Studies of the electronic noise and a drift velocity calibration procedure
Aleksei Dziuba (supervised by Prof. Alexey Vorobyev) / PNPI NRC KI
10th of June, 2020

## Slide 2: Goals of today’s talk
To demonstrate how TPC works on the example of the drift velocity calibration, which is needed for the absolute cross section measurement.
  At CERN only relative measurement is foreseen (AFAIK), but may be we have to think about absolute one.
  In Mainz an absolute measurements will be done.
Show that the maximum position of the Flash ADC spectrum is quite a good time-point estimate.
Present a data-driven method and a tool to generate electronic noise on even-by-event basis.
  https://github.com/aleksha/electronic-noise (Python with numpy, scipy and matplotlib)

## Slide 3: Calibration of drift velocities
Triggering from incoming beam electron. Time between beam and TPC response is known (with a precision discussed today).
MAMI has excellent beam. The ionization-anode distance is known with 0,1 mm precision.
titanium

## Slide 4: Conditions
720 MeV electrons as a beam
Simplified model
  Silicon detectors at entrance and exit.
  Scintillator at exit
  Ti windows
  H2, 20 atm as a single volume
Geant-4 with standard physics lists
Energy deposit at each tracking step is uniformly (not Poisson!) distributed along this step. 36,5 eV to create electron-ion pair
Ionization electrons are projected into anode plane (no loss assumed!).
Electronic response function + electronic noise

## Slide 5: Final GEANT Model
720 MeV electrons
Ti, 0.5 mm
H2 (20 atm.)
700 mm
y
z
Si, 0.25 mm
Scintillator, 10 mm
Si, 0.25 mm
Scintillator, 10 mm (removed in last versions)
+350 mm
-350 mm
This is simulation frame. TPC frame is rotated.
50 mm gaps between detectors as well as between detector and berylliums
0 mm
Ti, 0.5 mm
Beam is uniformly distributed in a circle with radius of 0,1 mm
No angular beam divergence!

## Slide 6: All pads
1
3
2
5
4
6
7
9
8
10
15
14
12
13
16
11
Central pad is a circle with 1 cm radius
Others are half-rings with 4 cm width
Numbering as on sketch
X
Beam
0

## Slide 7: Z distributions vs pad#
1
2
16
15

## Slide 8: Electron drift velocity in H2
Cathode-Grid
Grid-Anode
Known with few % accuracy, but we need 0,1% precision. We have to measure it!

## Slide 9: Simulation of drift process and electronics
Simulation frame (x,y,z)  Main experiment frame (X,Y,Z)
  z  X; y  Y; x  Position – Z
Drift velocities:
  W1 = 4,00 mm / microsecond
  [Cathode-Grid]
  W2 = 7,50 mm / microsecond
  [Grid-Anode]
Signal shaping as in test runs
(provided by Gennady Petrov)

## Slide 10: Modification of the response functions
Current on anode appears, when an electron arrive to the grid.
It increases linearly and ends, when the electron reach anode.
T Grid-Anode = L Grid-Anode / W2
An integral of the current is the charge of one electron (e = 1.602176634×10−19 C).
Response function of pre-amplifier must be changed according to this process
Anode
Grid
1e–
0 mm
10 mm
L Grid-Anode
L Grid-Anode / W2
0
Current, A
Time, s
2 × e × W2 / L Grid-Anode

## Slide 11: An electronic response function
Signal appears when electron reach anode
Current during Grid-Anode drift
For the previous simulation an electronic response appears, when an electron reach anode. Simple shift of the response function.
In a new version it starts, when an electron reach grid. Convolution with linear function (see previous slide).
Zero time – time, when electron is on the grid
L GridAnode = 10 mm; W2 = 7,5 mm/μs

## Slide 12: Flash ADC spectra for 25k events (no electronic noise)
Pad 01
Pad 16
No diffusion
With longitudinal diffusion
(see next slide)

## Slide 13: Longitudinal diffusion of electrons
σZ = 0,008 × √LTrackGrid
[σZ] = [LTrackGrid] = cm
Parametrization by German Korolev (private communication via Alexey Vorobyev)
Smear Z-position for each ionization electron by a Gaussian function with σZ.
LTrackGrid = 25 cm
10000 of beam electrons (a part of spectrum around the peak is presented)
What should be used as a time-point estimator?
With longitudinal diffusion
No diffusion

## Slide 14: Closer look
Ratio = No diffusion / With diffusion
Maximums are quite close

## Slide 15: Find maximum with pol2-fit
Maximum positions
With diffusion: 62317,9 ns
No diffusion: 62315,6 ns
2,3 ns difference at central (small) pad

## Slide 16
Only this pad contains electronics' noise
Only this pad contains electronics' noise
A scatter around a smooth curve indicates the accuracy of the estimate!
A bias for the maximum position estimator is on nanosecond-scale. Good enough!

## Slide 17: Noise studies
Done with ACTAF for a sample triggered by alpha-particles for the pads, which are far from alpha track.
Many thanks to Alexander Inglessi for the sample
Fast Fourier transformation shows that there some “featured” frequency channels
See a report: https://github.com/aleksha/electronic-noise/blob/master/docs/MC4NOISE.docx

## Slide 18: Noise generation
Obtain distributions for real and imaginary part of frequency spectra using Fourier transformation;
Fit these distributions using two gaussian hypotheses;
Generate random spectrum out of these distributions;
Use inverse Fourier transformation to obtain spectrum of generated events.
Example for one of frequency channel
Data-Model comparison

## Slide 19: Further studies of noise + simulation
Noise in data (baseline corrected)
Generated noise
Obtain distributions for real and imaginary part of frequency spectra using Fourier transformation;
Fit these distributions using two gaussian hypotheses;
Generate random spectrum out of these distributions;
Use inverse Fourier transformation to obtain spectrum of generated events.

## Slide 20: Energy calibration
Now we have 14-bit Flash ACD with 40 ns per time channel, which encode voltage in a range (-2,5, +2.5) mV
Additional calibration is needed to have same response for the signal and for the noise.
Done using alpha source.
5,5 MeV alpha-particle create a signal with integral of 200000 ADC channels (private communication with Alexander Inglessi)
A fake 1 mm track with 5,5 MeV energy deposit is created
It produces 150684 ionization electrons in a GEANT model
Integral for the Flash ADC spectrum is 152022
1 electron has “weight” = (200000 / 152022)

## Slide 21: Flash ADC spectrum with noise (Pad 2)
10 beam electrons
100 beam electrons
1000 beam electrons
10000 beam electrons
Relative electronic noise is suppressed by an increase of the cumulative statistics
Current procedure is quite slow
½ noise event / second for one CPU core

## Slide 22: Cumulative noise baseline corrected spectrum
100k noise events
Is it a fluctuation or an issue?
No clear answer yet, but that is not important for the drift time measurements, as well as for single events!

## Slide 23: 100k with noise
Pad 02
No diffusion
With longitudinal diffusion

## Slide 24: Maximum (peak position) shift due to noise
Peak is placed to the random location of cumulative noise spectrum
Shift of maximum for signal + noise (blue) wrt. pure signal (green)
Some fit examples

## Slide 25: Distribution for shifts for 100k events
100 random places for signal peak at the noise spectrum. Signal shape at the peak region and cumulative noise spectra are same, but position is different!
RMS for maximum with peak position fitting procedure 6,7 ns
Mean value for signals in the range ( Bin of maximum +/- 10 bins) is very dangerous estimator RMS = 17,9 ns)

## Slide 26: Summary
A drift velocity measurement is possible with several nanoseconds precision
6 ns precision / 60000 ns drift time  10–4 accuracy!
There are a procedure and a tool, which allow to create an electronic noise on event-by-event basis with a data-driven method.
  https://github.com/aleksha/electronic-noise (Python with numpy, scipy and matplotlib)
We can create signal with a noise now!